## Slide 1: ECE 382 Lesson 13
Lesson Outline
  Peripherals
  Memory-Mapped IO
  Ports
  GPIO
  Multiplexing

## Slide 2: Peripherals
What are Peripherals?
MSP430G2xx Peripherals?
  MSP430 wikipedia:
  Watchdog Timer
  Universal Serial Communication Interface (USCI)
    Implements SPI and I2C protocols
    We'll use SPI to interface with the LCD in your black box
  Pulse Width Modulation (PWM)
    We'll use this later to drive the robot
  Temperature Sensor
  Multipliers
  Capacitive Touch I/O
    For working with touch screens, etc

## Slide 3: Ports
What are Ports? Examples?
Your LaunchPad Board has…
  Port 1, Pin 0 to Pin 7
  Port 2, Pin 0 to Pin 5 (where are pin 6 and 7?)

## Slide 4: 68HC12

## Slide 5: Multiplexing
Only 20 Pins !!! But want access to many more signals
  Therefore, each pin shares several signals  multiplexing
Use PxSEL1 and PxSEL2 to select signal for each pin
  The details are in the MSP430G2x53 2x13 Mixed Signal MCU Datasheet.

## Slide 6: Pitfall !!!
Let's say I wanted to make the UCA0SOMI function available on P1.1:
  ; 'from USCI' means this bit is set automatically by the USCI when enabled
  bis.b #BIT1, P1SEL
  bis.b #BIT1, P1SEL2

## Slide 7: How do we talk to Ports? Do I/O?
Two classic methods
  Memory-Mapped I/O (Motorola)
  Port-Mapped I/O [or Isolated IO] (Intel)
Memory-Mapped I/O
  I/O and memory SHARE the same address space
  Advantage
    Fewer instructions
    Can use all addressing modes
  Disadvantage
    Lose memory to IO
    Programmer mistakes
  How to use
    mov.b #0x55, &P1OUT
    mov.b #0x55, &0x0021
  User’s Guide p 333, Table 8-2 (BB pp 41)
  Watchdog Timer, page 341 (BB pp 42)

## Slide 8: How do we talk to Ports? Do I/O?
Port-Mapped I/O (Intel)
  I/O and memory have their own separate address space
  Advantage
    Don't lose memory for IO.
    Protects coder from mistakes.
  Disadvantage
    Need More Instructions (like In/Out)
    More restrictive addressing modes
    Works only with limited registers
  How to use
    Out #0x55, &PORT1

## Slide 9: General Purpose Input Output (GPIO)
The registers used to configure GPIO are PxDIR, PxREN, PxOUT, and PxIN
  PxDIR configures which pins are input and which pins are output
    1 corresponds to output, 0 to input
  PxREN controls pull up / pull down resistors to avoid floating inputs.
  Writing to PxOUT controls the output of each pin
  PxIN allows you to read the values on these pins
Let's write a program that controls the onboard LEDs with the onboard push button
bis.b #BIT0|BIT6, &P1DIR
bic.b #BIT3, &P1DIR
check_btn: bit.b #BIT3, &P1IN ;push button is LOW on push
jz set_lights
bic.b #BIT0|BIT6, &P1OUT
jmp check_btn
set_lights: bis.b #BIT0|BIT6, &P1OUT
jmp check_btn
Any problem with this code?
Family Users Guide p 328
Blue Book pp 38

## Slide 10: Example Program
Input was FLOATING! Low is ground, High is floating, so use a pull- _________?
bis.b #BIT0|BIT6, &P1DIR ; output pin direction
bic.b #BIT3, &P1DIR ; input pin direction
bis.b #BIT3, &P1REN ; enable pin 3’s resistor
bis.b #BIT3, &P1OUT ; make it a pull-up? (trick)
check_btn: bit.b #BIT3, &P1IN
jz set_lights
bic.b #BIT0|BIT6, &P1OUT
jmp check_btn
set_lights: bis.b #BIT0|BIT6, &P1OUT
jmp check_btn
Modify code to toggle the LEDs when button is pressed (i.e. one LED on and one off)

## Slide 11
Figure 1.23 Logic levels and noise margins
Why Pullup and Pulldown Resistors are needed
Voltage Levels and Noise Margins

## Slide 12: Pitfall !!!
Anything wrong with this?
  mov.b #0xff, P1DIR
What do these commands do?
  mov.b #0b00001111, &P1DIR
  bis.b #0b00001111, &P1OUT
  mov.b #0xff, &P1OUT
  mov.b &P1IN, r5

## Slide 13: Inclass Exercise
Modify this program so the two LEDs always have the opposite value
bis.b #BIT0|BIT6, &P1DIR ; output pin direction
bic.b #BIT3, &P1DIR ; input pin direction
bis.b #BIT3, &P1REN ; enable pin 3’s resistor
bis.b #BIT3, &P1OUT ; make it a pull-up? (trick)
check_btn: bit.b #BIT3, &P1IN
jz set_lights
bic.b #BIT0|BIT6, &P1OUT
jmp check_btn
set_lights: bis.b #BIT0|BIT6, &P1OUT
jmp check_btn