## Slide 1: ECE 382 Lesson 21
Readings
  Everything You Need to Know About Pointers in C
  Short, Funny Pointer Video
Lesson Outline
  Pointers
  Arrays
  Function Parameters
  Practice
Admin
  Assignment 7 due next Lesson
  KSplice pointer challenge (optional, but kind of fun)

## Slide 2: C Language: Pointers
Pointer: A pointer is a variable that holds a memory address.
An address “points” to a value in memory.
In assembly: mov 0(r5), r6 ; is r5 or r6 the pointer?
Examples:
int x = 0x1234, y= 0x5678; //assume put at 0x200
int *xPtr;
int *yPtr;
xPtr = &x; //what is in xPtr?
y = *xPtr; //what is in y?
x = y; //what is in x?
*xPtr = 0x2019; //what is x?
xPtr = 0x0206;
*xPtr = y; //where is this stored?
Token | Context | Description
& | Assignment statement | Returns the address of the variable after this token
* | Variable declaration | Variable contains the address pointing to a variable of type var_type
* | Assignment statement | Allows you to access the contents of the variable at which the pointer is pointing
-> | Structure | Access a structure's elements through a structure pointer (instead of the "." notation). Also can use (*structure).element.
Addr | Value
0x200 | 
0x201 | 
0x202 | 
0x203 | 
xPtr | 
x | 
y | 

## Slide 3: C Language: Pointers
Examples:
int a = 10; // declaring an integer
int * aPtr; // declaring a pointer to an integer
struct point {
char x, y;
};
aPtr = &a; // setting the value of aPtr to the address of a
*aPtr = 20; // sets a to 20 by dereferencing aPtr
struct point myPoint = {1,2}; // declaring a structure of point_t, initializing
// with constants
struct point * myPointPtr; // declaring a pointer to a point_t
myPointPtr = &myPoint; // setting the value of myPointPtr to address of
// myPoint
myPoint.x = 5; // sets myPoint.x to 5
(*myPointPtr).x = 10; // sets myPoint.x to 10 by dereferencing myPointPtr
myPointPtr->x = 20; // sets myPoint.x 10 20 by dereferencing myPointPtr
// (alternative method)

## Slide 4: C Language: Pointers
Examples:
unsigned char x = 0x25; // address of x is 0x1000
unsigned int y = 0x1234; // address of y is 0x1001 - 0x1002
unsigned char* xPtr = &x; // address of xPtr is 0x1003 - 0x1004
unsigned char* yPtr = &y; // address of yPtr is 0x1005 - 0x1006
Examples: // Questions are independent - reset variables
to original state
xPtr++; // xPtr = ?
x = *xPtr + 1; // x = ?
// Reset variables to original state
*xPtr = 0x12; // x = ? xPtr = ?
// Reset variables to original state
y = yPtr + *yPtr; // y = ? yPtr = ?
Addr | Value
0x1000 | 
0x1001 | 
0x1002 | 
0x1003 | 
0x1004 | 
0x1005 | 
0x1006 | 
0x1007 | 

## Slide 5: C Language: Arrays
Array: a collection of elements of the same data type stored in consecutive memory locations.
Index counting starts at 0
Max index is NUM_ELEMENTS - 1
  <data_type> array_name[NUM_ELEMENTS]; // Uninitialized
  <data_type> array_name[] = {val0, val1, ...}; // Initialized
array_name decays into a pointer to the first element in the array
<data_type> lets the compiler know how much to "jump" between elements in the array
Examples:
unsigned int a[3]; // address of a[0] is 0x1000,
// address of a[1] is 0x1002,
// address of a[2] is 0x1004
unsigned int* myPtr; // myPtr is 0x1006
unsigned int x;
a[0] = 0x1234;
a[1] = 0x5678;
a[2] = 0x9ABC;
x = a[0];
myPtr = a; // can I do this?
x = *myPtr;
x = myPtr[1];
x = *(myPtr + 2); // tricky?
a = myPtr; // you can’t do that
Addr | Value
0x1000 | 
0x1001 | 
0x1002 | 
0x1003 | 
0x1004 | 
0x1005 | 
0x1006 | 
0x1007 | 
0x1008 | 
0x1009 | 

## Slide 6: C Language: Function Parameters
Pass by Value - Passing the actual value of the variable ( pass a copy )
Good choice for small-sized variables
Expensive to copy larger variables (e.g. structures, arrays, etc.)
Pass by Pointer - Pass pointer into variable (same as Pass by Reference) ( pass access to the original )
Constant size parameter no matter how large the object it is to point to
Allows you to directly modify the variable in the function without a return statement
Pass by Value Example:
char x=5; y=10;
z = some_function(x, y)
…
char some_function(char a, char b) {
a += 5; b += 5; // does this change x and y?
return a + b;
}
Pass by Reference Example:
char x=5; y=10;
z = some_function(&x, &y)
…
char some_function(char* a, char* b) {
*a += 5; *b += 5; // does this change x and y?
return *a + *b;
}

## Slide 7: C Language: Practice
char x; // Memory location 0x0800 = 0xFF
char y[3]; // Memory locations: 0x0801 = 0x23, 0x0802 = 0x56, 0x0803 = 0x89
char* letter_ptr; // Memory locations: 0x0804 - 0x0805 = 0xABDC
Question: What values would be assigned using the following statements?
// Questions are independent - reset variables to original state
x = y[2];
// Reset variables to original state
letter_ptr = y;
x = *(letter_ptr + 2);
// Reset variables to original state
letter_ptr = &x;
y[2] = *(letter_ptr + 1);
Addr | Value
0x800 | 
0x801 | 
0x802 | 
0x803 | 
0x804 | 
0x805 | 
Addr | Value
0x800 | 0xFF
0x801 | 
0x802 | 
0x803 | 
0x804 | 
0x805 | 
Addr | Value
0x800 | 0xFF
0x801 | 0x23
0x802 | 0x56
0x803 | 0x89
0x804 | 
0x805 | 
Addr | Value
0x800 | 0xFF
0x801 | 0x23
0x802 | 0x56
0x803 | 0x89
0x804 | 0xDC
0x805 | 0xAB
// x = 0x89
// letter_ptr = 0x0801
// x = 0x89
// same as x = letter_ptr[2]
// letter_ptr = 0x0800
// y[2] = *(0x800 + 1) = 0x23

## Slide 8: Writing Clean Code
Meaningful Names
Use intention-revealing names ("self-documenting")
  int d, temp; // elapsed time in days, a temporary variable
  int elapsedTimeInDays, daysSinceModification;
Make meaningful distinctions
  void copyChars(char* a1, char* a2)
  void copyChars(char* source, char* destination)
Use pronounceable names
  DtaRcrd
  DataRecord
Use searchable names
  MAX
  MAX_STUDENTS
Functions: use verbs!
  forward()
  moveForward()
Don't be cute
  holyHandGrenade()
  deleteItem()
Pick one word per concept
  Bad: fetch(), retrieve(), get()
Okay to use i, j, k for loop counters

## Slide 9: Clean Functions
Small - ideally less than 10 lines long
Do one thing
Use descriptive names
Parameters: rarely need more than two or three
Side effects - function should only do what you say it does
Do not use static or global variables
Only depend on local variables / parameters
Don't repeat yourself - write a function instead of copy / paste
Only one entry / exit point
Indent correctly!

## Slide 10: Clean Comments
Comment on "big picture" items
  Head of each file
  Definition of each function
  Beginning of each major block of code
As you move deeper in the hierarchy, the comments are more specific
Try writing functions / meaningful names
  if ((employeeFlags & HOURLY_FLAGS) && (employeeAge > 65)) ...
  if (isEligibleForFullBenefits(employee)) ...
TODO comments
  // TODO: Make this into a function
  // TODO: Write new header file to group these functions
Bad comments
  Restating your code (a = 1; // Setting a to 1)
  Commented-Out code
  Too much information
  Don't comment bad code - rewrite it.